## Slide 1: SOC Final Project Group 3: Drone-Aided Police Control System
Group Member:
工科所 109011566 楊智勝
資工所 111062656 許芷毓
交大電信所 0007-310513008 楊士緯
電機系 108061181 郭義安
光電所 110066534 陳俊翰

## Slide 2: Outline
Introduction
System Architecture
Specification and Technology Analysis
  Drone system
  Camera - Electronic Image Stabilization (EIS)
  AI algorithm
  Edge server
Industrial Analysis
  Porter’s 5 force analysis
  S.W.O.T analysis
Conclusion
Task Partition
References

## Slide 3: Outline
Introduction
System Architecture
Specification and Technology Analysis
  Drone system
  Camera - Electronic Image Stabilization (EIS)
  AI algorithm
  Edge server
Industrial Analysis
  Porter’s 5 force analysis
  S.W.O.T analysis
Conclusion
Task Partition
References

## Slide 4: Introduction
We propose a drone-aided police control system, which assist the police for real-time surveillance on big events
Target market
  Police, event host, telecom operator (CHT, FET, TWM)
Application scenarios
  Concert, new year eve’s party, baseball game
  Traffic jam during commute time

## Slide 5: Motivation
Itaewon crowd crush (梨泰院)
  It’s difficult for the police to rescue since the space is full people
To prevent the tragedy happens again
  We aim to propose a framework provide a better efficiency to evacuate crowd

## Slide 6: Outline
Introduction
System Architecture
Specification and Technology Analysis
  Drone system
  Camera - Electronic Image Stabilization (EIS)
  AI algorithm
  Edge server
Industrial Analysis
  Porter’s 5 force analysis
  S.W.O.T analysis
Conclusion
Task Partition
References

## Slide 7: System Architecture

## Slide 8
Edge server
Crowd density recognition
Traffic analyze
Drones management
Drone with LED & speaker
Drone with projector & speaker
Drone with 5G small cell
GPS, Video, and RSS data
Control signal
GPS data
Traffic light
Monitor
Control signal
Video data
Warning message
Data Flow

## Slide 9: Outline
Introduction
System Architecture
Specification and Technology Analysis
  Drone system
  Camera - Electronic Image Stabilization (EIS)
  AI algorithm
  Edge server
Industrial Analysis
  Porter’s 5 force analysis
  S.W.O.T analysis
Conclusion
Task Partition
References

## Slide 10: Drone System (1/10)
SoC specification
We adopt the 5G solution from Mediatek
  MediaTek Dimensity 9200
Camera
  CMOS sensor: 1/1.2 inch, 12MP
  Angle of view: 82.1 degree
  Aperture: f/1.7

## Slide 11: Drone System (2/10)
5G radio band: 4.4GHz ~ 4.7 GHz
  This frequency band is exclusive to the police
MediaTek Dimensity 9200’s powerful performance ensure the quality of videos
  Its cutting-edge display technology supports FHD+ up to 240Hz
  MediaTek AI-SR/MEMC provides best-in-class video streaming

## Slide 12: Drone System (3/10)
Sensors
Gyroscope
  Calculate the tilt angle of the body and is an indispensable sensor stabilizing
Barometer
  Sense the relative and absolute height of an object through changes in air pressure
Accelerometer
  Sense the magnitude and direction of combined linear and gravitational acceleration
GPS
Magnetic field orientation sensor (magnetometer or compass)
  Sense the earth's magnetic field (geomagnetism), so as to know the direction of the drone face to
Notes: Introduction of drone sensors

## Slide 13: Drone System (4/10)
Consists of three kinds of drone
  Drone equipped with projector, flash light, speaker, and 5G small cell, respectively
Projector
Inspired by the Google patent – placing a screen on a drone
We placed a outdoor projector screen rather than a screen
  To reduce the loading of the drone
We adopt the product from Elite Screens
  The Yard Master Electric
Product features
  Designed for outdoor use without compromising its home theater visual appeal
  Wide diffusion uniformity allows viewers to enjoy a clear and bright picture from any angle

## Slide 14: Drone System (5/10)
The screen provide the information to evacuate

## Slide 15: Drone System (6/10)
Flash Light
DJI Mavic air 2 mini pro flash light
  Maximum power: 10 W
  Battery Capacity: 380 mAh
  Working time:
    Single flash: 6h
    Dual flash: 3h
  Brightness (lumens): 1000 Lm

## Slide 16: Drone System (7/10)
Combine multiple drone’s LED to generate different pattern
Simp4live Records (a musical group)
  Specializing in light sculpture shows
The pattern generate by the drones can guide the crowd where to evacuation
  E.g., form an arrow shape to navigate the direction

## Slide 17: Drone System (8/10)
Speaker Specification
 | Spec
Brand name | Global Drone
Speaker controller battery | 3.7 V, 800mAh
Speaker action time | About 2 hours
Speaker size | 13.5 *10.2* 3.8 ()
Speaker weight | 95g
Control distance | 1000m
 | Spec
Brand name | Global Drone
Speaker controller battery | 3.7 V, 800mAh
Speaker action time | About 2 hours
Speaker size | 
Speaker weight | 95g
Control distance | 1000m

## Slide 18: Drone System (9/10)
5G Small Cell
Due to the physical characteristic of high frequency signal and the demand of 5G signal
  It is necessary to extend the signal coverage for 5G network to achieve low latency, high data rate
Small cell is a major feature for 5G network
  To deal with the short communication range of 5G network
  It enables network to extend coverage and to deliver low latency

## Slide 19: Drone System (10/10)
Cell on Wings (COW) – Flying COW
  Increase the coverage of mobile signal from the sky
AT&T launched their COW technology in 2022 – 5G Flying COWs
  The drones with a tether to the ground that provides power and fiber optic cable to broadcast data
Chunghwa Telecom (CHT) and THUNDER TIGER have proposed COW application

## Slide 20: Camera - Electronic Image Stabilization (EIS) (1/2)
An image enhancement technique that effectively adjusts and balances the captured image
The system includes a sensor integrated into the camera
  Reducing jittering and capturing the best stable photos
EIS incorporates two techniques to make the image stable
  It digitally zooms in to capture a more prominent image
  It corporates a larger sensor to resize the image to fit the available space (hardware-based)
Compare with the optical image stabilization (OIS) method
  EIS has a better stabilize performance
  EIS keeps improving the appearance through equal shifting, whereas the gimbal stabilizer works only drone has shifted

## Slide 21: Camera - Electronic Image Stabilization (EIS) (2/2)
How EIS work?

## Slide 22: AI Algorithms - Crowd Density Recognition (1/3)
Combined both RGB image and received signal strength (RSS)
  To deal with the low quality images, such as occlusion, or poor light condition
Received signal strength (RSS)
  A measurement of the power in a received radio signal
  It can be measures from each received packet in the MAC layer
  It can be described how far a person is from the UAV
The original RSS is transform into the human density map (RDM)

## Slide 23: AI Algorithms - Crowd Density Recognition (2/3)
The model (RIFNet) has been divided into two branch
  The image-based branch and the signal-based branch
The overall architecture

## Slide 24: AI Algorithms - Crowd Density Recognition (3/3)
The performance of RIFNet is better than the state-of-the-art methods
The scenario is as follows:
After obtain the crowd density
  We set a threshold to decide whether the density is overloaded or not to prevent a crowd crush

## Slide 25: AI Algorithms - Traffic Analysis (1/2)
The system can analyze the traffic
  Based on the video captured by drone and deep learning method
We adopt the You Look Only Once version 5 (YOLOv5) model
  To deal with the object detection task
  It identifies objects more rapidly and more precisely than other recognition systems

## Slide 26: AI Algorithms - Traffic Analysis (2/2)
We estimate the speed of each object from the object detection results
If several objects’ speed is lower than a threshold, a traffic jam may occur
  Adjust the duration of the traffic light

## Slide 27: Processing Flow

## Slide 28: AI Algorithms - Drone Management (1/3)
The advantages of AI-based autonomous drone
  The system is cheaper and safer since no human error

## Slide 29: AI Algorithms - Drone Management (2/3)
AI-powered flight controller
An AI-powered flight controller is necessary that has the right types of sensor
Capable of following a preprogrammed flight path and therefore perfect for autonomous navigation
Positioning system
Depend on our GPS and vision-based methods
Path planning for multi-drone system
By considering several information
  Battery recharge time
  Battery capacity
  Arrival time at each node
  Position
  Crowd density
  Objectives of other drones

## Slide 30: AI Algorithms - Drone Management (3/3)
General Drone Scheduling Problem (GDSP)
One of the key problems that have received increasing attention over the last decade
Associate with several features
  Such as launch points, nodes, objectives, monitoring, and battery capacities
Under the limited amount of the flying time
  The drone is designed to served the designated customers and return the launch point
We plan to use GDSP to help with the task of calculating flight paths
GDSP is basically a set of rules and constraints
  That make sure the path planning is in the most optimized way

## Slide 31: Edge Server
The AI algorithms is computed by the edge server
Upgraded from W332-Z00 AMD Ryzen™ Tower Entry Workstation
Specification | 
Motherboard | MC13-NB0
Memory | 256gb DDR5
CPU | AMD EPYC™ 9004
GPU | NVIDIA A100 40/80GB PCIe GPU
Power Supply | Cosair AX1600i

## Slide 32: Outline
Introduction
System Architecture
Specification and Technology Analysis
  Drone system
  Camera - Electronic Image Stabilization (EIS)
  AI algorithm
  Edge server
Industrial Analysis
  Porter’s 5 force analysis
  S.W.O.T analysis
Conclusion
Task Partition
References

## Slide 33: Porter’s 5 Force Analysis
Bargaining power of customers
Low, our product is very innovative and is specifically designed for use by the police.
Bargaining power of suppliers
High, many patents or technologies are only offered by a single manufacturer.
Threat of new entrants
Low, our product is mainly designed for the police and is not easily accessible for the general public to purchase.
Threat of substitutes
Low, our product is designed by combining the technologies and patents of different manufacturers and is mainly for use by the police.
Competitive rivalry
None, there are no competitors in the market.

## Slide 34: S.W.O.T Analysis
Strength
  Product is unique
  Applications such as Sim4live Records first been used on evacuation
  A variety of option for different scenarios (speaker, projector, and LED)
Weakness
  Only suitable for the police
  Expensive
Opportunities
  The product can be sold to police in other countries
  Military surveillance applications
  Rent to the organizer of big event
Threat
  Privacy and security issues
  DJI rescue services

## Slide 35: Outline
Introduction
System Architecture
Specification and Technology Analysis
  Drone system
  Camera - Electronic Image Stabilization (EIS)
  AI algorithm
  Edge server
Industrial Analysis
  Porter’s 5 force analysis
  S.W.O.T analysis
Conclusion
Task Partition
References

## Slide 36: Conclusion
In this work, we propose a drone-aided police control system to assist the police task
The system provides a way to evacuate the crowd when an emergency occurs
It broadcast the alert by speaker, projector, etc.
  Everyone can notice the alert from the sky and the crowd can be evacuated with a more clear instruction
The system also provide a traffic analysis in real-time
  Control the traffic light when a traffic jam is appear
The industrial analysis shows the novelty of the proposed system
The weight of the drone and the battery life is the points that can improve in the future

## Slide 37: Task Partition
Proposal - All
SoC specification - 許芷毓
Technology analysis
  Drone - 陳俊翰
  Camera - 楊士緯
  LED, projector, speaker - 楊智勝
  Edge server - 郭義安、陳俊翰
  5G communication - 許芷毓
  Drone management and path planning algorithm - 郭義安
  Monitoring system (crowd density) and traffic analysis algorithm - 楊士緯
  Industrial analysis - 楊智勝
Organize report - 楊智勝、許芷毓
Presentation - 楊士緯、郭義安、陳俊翰
Note that the task partition is described with more detail in the final report

## Slide 38: References (1/4)
Wikipedia-Seoul Halloween crowd crush https://en.wikipedia.org/wiki/Seoul_Halloween_crowd_crush
CNN-‘Somebody is going to die’: How Seoul’s deadly Halloween crush unfolded. https://edition.cnn.com/2022/11/04/asia/itaewon-seoul-korea-halloween-crush-timeline-intl-hnk-dst/index.html
156 die in Halloween crowd crush in Korea's Itaewon https://koreajoongangdaily.joins.com/2022/10/30/national/socialAffairs/Korea/20221030191108962.html
Camera https://www.allaboutcircuits.com/technical-articles/introduction-to-cmos-image-sensors/ https://www.dronescend.co.uk/blogs/news/electronic-image-stabilisation
Introduction to RSS: https://info-nrlte.com/2021/05/09/an-introduction-to-csi-rs/
RIFNet: Kai-Wei Yang, Yen-Yun Huang, Jen-Wei Huang, Ya-Rou Hsu, Chang-Lin Wan, Hong-Han Shuai, Li-Chun Wang, and Wen-Huang Cheng. 2022. Improving Crowd Density Estimation by Fusing Aerial Images and Radio Signals. ACM Trans. Multimedia Comput. Commun. Appl. 18, 3, Article 84 (August 2022), 23 pages.
Traffic analysis: H. Zhang, M. Liptrott, N. Bessis and J. Cheng, "Real-Time Traffic Analysis using Deep Learning Techniques and UAV based Video," 2019 16th IEEE International Conference on Advanced Video and Signal Based Surveillance (AVSS), 2019, pp. 1-5.
YOLOv5: https://blog.roboflow.com/yolov5-improvements-and-evaluation/ https://www.researchgate.net/figure/YOLOv4-Tiny-network-architecture-based-on-CSPDarknet53-Tiny-backbone-and-CSPBlocks_fig2_360985952
https://pedin024.medium.com/初探yolov5-71f13b4ba78d
論無人機商用服務與整合技術 http://www.cie.org.tw/cms/JournalFiles/10912_chapter07.pdf

## Slide 39: References (2/4)
Qualcomm® QRB5165 SoC for IoT Product Brief https://www.qualcomm.com/content/dam/qcomm-martech/dm-assets/documents/qrb5165-soc-product-brief_87-28730-1-b.pdf
Qualcomm’s latest drone platform features 5G and seven cameras https://linuxgizmos.com/qualcomms-latest-drone-platform-features-5g-and-seven-cameras/
Qualcomm-5G https://www.qualcomm.com/5g/what-is-5g#:~:text=Q%3A%20What%20is%205G%3F,machines%2C%20objects%2C%20and%20devices.
Wikipedia-5G https://en.wikipedia.org/wiki/5G
Digi: Comparison between 4G vs 5G https://www.malaysiainternet.my/2019/04/digi-comparison-between-4g-vs-5g/
EMF-5G EXPLAINED - HOW 5G WORKS https://www.emfexplained.info/?ID=25916#How%20does%205G%20work
LITEPOINT- An Introduction to the 5G Small Cell https://www.litepoint.com/blog/an-introduction-to-the-5g-small-cell/
iThome- 9個QA快速認識5G https://www.ithome.com.tw/news/138745
消防署） 「警消微波網路系統移頻計畫」 - 行政院 https://www.google.com/url?sa=i&rct=j&q=&esrc=s&source=web&cd=&ved=0CAMQw7AJahcKEwiws_Wj0aj8AhUAAAAAHQAAAAAQBQ&url=https%3A%2F%2Fwww.ey.gov.tw%2FFile%2F214A16AB14520C65&psig=AOvVaw3ir4H7r7mptTubitMzeUD9&ust=1672740280890298
MediaTek Dimensity 9200 with TSMC N4P, Arm Cortex-X3, and ray tracing is now released https://technewsrooms.com/mediatek-dimensity-9200-released/

## Slide 40: References (3/4)
Chipset for Incredible Performance and Unmatched Power Savings https://corp.mediatek.com/news-events/press-releases/mediatek-launches-flagship-dimensity-9200-chipset-for-incredible-performance-and-unmatched-power-savings
Wikipedia-Mobile cell sites https://en.wikipedia.org/wiki/Mobile_cell_sites
Youube-行動基地台車是什麼原理？直擊中央公園跨年現場！五大電信訊務擴充部署情形 & 4G/5G測速 https://www.youtube.com/watch?v=Q6J-I_E-uf8&ab_channel=%E6%84%9B%E8%93%81AiZhen
When COWs Fly: AT&T Sending LTE Signals from Drones https://about.att.com/innovationblog/cows_fly
How cell tower 'COW' drones will keep fans safe at the Super Bowl https://www.zdnet.com/home-and-office/networking/how-cell-tower-cow-drones-will-keep-fans-safe-at-the-super-bowl/
緊急空中基地台系統 https://www.taiwanexcellence.org/tw/award/product/109423
YouTube-【中華電信 + 雷虎科技】緊急空中基地台系統 Flying Mobile Base Station for Emergency Recovery https://www.youtube.com/watch?v=izmbLGrBWTk&ab_channel=ThunderTiger%E9%9B%B7%E8%99%8E%E7%A7%91%E6%8A%80
http://www.simp4live.com/projection-mapping-big/body-projection-mapping-vj-4hkbd
https://shopee.tw/DJI大疆御-Mavic-air-2-mini-2-pro爆閃燈-phantom精靈4夜航燈-閃光燈-10w警示燈-i.307929595.8605216889
https://urbenq.com/2016/08/12/google%e6%96%b0%e5%b0%88%e5%88%a9%ef%bc%9a%e7%94%a8%e7%84%a1%e4%ba%ba%e6%a9%9f%e6%90%ad%e8%9e%a2%e5%b9%95%e3%80%81%e6%8a%95%e5%bd%b1%e6%a9%9f%e4%be%86%e9%96%8b%e8%a6%96%e8%a8%8a%e6%9c%83%e8%ad%b0/

## Slide 41: References (4/4)
https://patents.google.com/patent/AU2016226595B2/en
https://elitescreens.com/products/yard-master-electric-series/
https://www.alibaba.com/product-detail/Global-Drone-Speaker-Portable-Drone-Megaphone_62558745815.html
https://zh.wikipedia.org/zh-tw/Bayraktar_TB2
https://zh.m.wikipedia.org/zh-tw/無人機表演
https://www.grandviewresearch.com/industry-analysis/consumer-drone-market

## Slide 42
Thank You!