## Slide 1: Health Monitoring IoT System for Vehicle
Group 4
111061580張睿紘 110061635 王瑞賢
111064559 徐詠祺 111065535 楊文彣
111064539 張文彥

## Slide 2: Outline
Introduction
  Motivations
  Target Applications
  Application Scenario
Evolution
System Architecture
Technology
  Sensors
  Tx & Rx
  DVFS
  AIoT System
Industry Analysis
Conclusion
References
Team Member task partition

## Slide 3: Motivation
The lack of awareness of vehicle maintenance
  Higher risk of nasty accident
  Spending more time and money to repair
The small vibration or signal for the early stage vehicles’ failure is hard to notice
Important information for
car insurance company

## Slide 4: Target Applications
Detects early-stage failures:
  Reduce the risk of breakdown
  Improve machine performance
  Extend machine use life
Scoring machine health and your driving habbits
Predicts failures:
  Predicting machine failure from
sensors detection and users’
driving style

## Slide 5: Application Scenario
Vehicle failure alert system
Usage Based Insurance

## Slide 6: Evolution

## Slide 7: System Architecture
Memory
Clock
ARM Cortex-M0+
(MCU)
EH-
PMU
Interfaces
(I2C, SPI, ADC)
WRX
Sensor
TRX
DSP
Ethernet Controller
Cloud Computing
User
Devices
FFT

## Slide 8: Technology
Sensors:
  Acceleration
  Temperature
  Humdity
Tx & Rx:
  IEEE 802.11ba
  Wake-up Radio receiver
Power management
  Microcontroller
  DVFS
  Energy Harvesting
Storage Device:
  Cloud Storage
Network
  LTE / Wi-Fi backhaul

## Slide 9: Sensors
Relative Humidity Sensor
Accelerometer
Magnetometer
Thermistor

## Slide 10: Relative Humidity Sensor
Capacitive humidity sensor
  Dielectric layer absorbing moisture from air
  Wide range detection from 0% to 100%
  Low power, Linear output, High stability
  Temperature dependence (combined with temp sensor)

## Slide 11: Accelerometer
Capacitive Accelerometer
  Movement changes capacitance between mass & comb fingers
  Proof of mass + Comb capacitor + Spring

## Slide 12: Magnetometer
Hall Effect Magnetometer
  Drift voltage caused by Lorentz force when a magnetic field is present
  Amplifier is needed due to small drift voltage
  Schmitt trigger to resist noise & bounce

## Slide 13: Thermistor
2 basic types:
Positive Temperature Coefficient (PTC)
Negative Temperature Coefficient (NTC)
Temperature range: −100 °C and 300 °C
Monitoring temperature by ADC

## Slide 14: Operation Flow
Target: continuous monitoring in varying condition
Extracting information on chip through calculation
Interface: I2C, SPI, ADC
Controller
Sensors
Cal Unit
(ex: FFT)
TX
wake
raw data
message

## Slide 15: Tx & Rx
Wake-Up Radio
IEEE 802.11ba
Wake-Up Radio system architecture
WuRx wake-up circuit

## Slide 16: Wake-Up Radio

## Slide 17: IEEE 802.11ba
July to November 2016, the scope and targets of the standard were defined. There are three key requirements:
The Wake-Up Radio (WuR) power < 1mW.
The WuR should coexist with legacy IEEE 802.11 devices in the same band.
The WuR should meet the same range requirement as the primary connectivity radio.

## Slide 18: Wake-Up Radio system architecture
The primary radio of an IEEE 802.11ba-capable low-power device is put to sleep in order to save energy
When the sleeping device is required, a packet is sent in order to generate a call to wake up the device’s primary radio

## Slide 19: WuRx wake-up circuit
An off-chip matching network to provide passive gain into the analog front-end
SAR ADC and digital baseband issue fast wakeup or secure wakeup signal to MCU

## Slide 20: Power Management
Microcontroller
DVFS
Energy Harvesting

## Slide 21: Microcontroller
Three Sleep modes
Normal Sleep
Deep Sleep
(Wake up Interrupt Controller (WIC))
Deep Sleep with State Retention Power Gating (SRPG) support (WIC + SRPG)

## Slide 22: Microcontroller
Feature of Cortex M0+ :
Similar size and programmer’s model to Cortex M0
Low gate count same as Cortex M0
Two-stage pipeline (more low energy consumption)
Memory Protection

## Slide 23: DVFS
DVFS is dynamic voltage frequency adjustment, and dynamic technology is to dynamically adjust the operating frequency and voltage of the chip
Adjustment Steps:
When power needs to be boosted
When power needs to be reduced
Increase the supply voltage
Increase the clock frequency
Reduce the clock frequency
Reduce the supply voltage

## Slide 24: Energy Harvesting
Multi-modal energy-harvesting power management unit
(EH-PMU) with supercapacitor
Harvest from:
EM (electromagnetic) coil
Photovoltaic (PV) cell
Thermoelectricgenerator (TEG)
Vibration
RF energy

## Slide 25: Automotive Ethernet
The automotive industry has adopted Ethernet for in-vehicle networking (IVN) based on open IEEE standards.
Notes: Cadence offers a variety of IP to support Automotive Ethernet applications (Figure 1). For example, you can design high-speed automotive Ethernet communication links between advanced driver assistance systems (ADAS), infotainment, cameras, and other electronic control units (ECUs) by leveraging the Cadence® Ethernet controller.

## Slide 26: Automotive Ethernet
10G/2.5G/1G Multi-Speed Ethernet Controller IP for Automotive Applications from Cadence
Notes: The Controller IP for Automotive is engineered to be quickly and easily integrated into any SoC. As shown below, the Controller IP for Automotive connects to a PHY through standard media independent interfaces such as MII, RMII, GMII, RGMII, XGMII, SGMII, or USXGMII. The host layer access to the Controller IP for Automotive is through industry-standard AXI or AHB interfaces when the DMA is being used or through an external FIFO interface. A separate APB interface allows the host applications to configure the Controller IP for Automotive.

## Slide 27: Communication Protocols
Notes: LIN Protocol: LIN stands for Local Interconnect Network; it is a serial communication and low-cost protocol for various low speed and non-critical electronic applications in an automobile. It is a master-slave type of communication based on polling strategy (like UART) and it is half-duplex or one way communication at a given time. There are 1 Master and up to 15 slaves on a LIN bus. The communication between Master and Slaves happens through a fixed frame structure initiated by the master always. The slave/(s) respond to the header accordingly. It is important to note that, sometimes the master can respond to its own header.
CAN Protocol: CAN stands for Controller Area Network, which is a serial communication protocol supporting distributed real-time control with a very high level of security and efficiency. It is a broadcast type of protocol, in which the concept of ‘Master’ and ‘Slave’ is not present. The communication between nodes happens in a fixed frame structure. Any device/node having an update over a specific activity from any application could transmit the corresponding frame and every other device/node on the bus could read this frame and respond to it correspondingly. During such a situation, conflict on the bus is inevitable. This is resolved by ‘bit-wise arbitration’.
FlexRay Protocol: FlexRay is a fault-tolerant, deterministic, and high-speed automotive networking serial communication protocol. The fundamental idea of designing the FlexRay protocol was to meet the high-speed requirements of various applications in an automobile. Even in this protocol, there are multiple nodes trying to communicate and there is no master slave concept present. Each node is given a specific time during which the communication happens. A fixed frame structure is used to communicate between the nodes.

## Slide 28: Neural Network
Improved BP (Back-propagation) Neural Network
The average absolute error of the traditional BP neural network algorithm is 0.5976, The average absolute error of the traditional BP neural network algorithm is 0.5976
Notes: WCMC_2287776 1..11 (hindawi.com)

## Slide 29: Neural Network
Software IP and data that needs protection are stored as encrypted hash to ensure security

## Slide 30: Outbound Data Flow
AT&T In-Car WiFi
  An Internet data plan working with your vehicle’s built-in Wi-Fi hotspot
  In-car Wi-Fi turns your vehicle into a Wi-Fi hotspot with fast, reliable internet access even when you’re far from home.
  The collected components’ data are sent through WiFi to the data center for predicting component failure.
Notes: Most new cars in 2020 come with either embedded (built-in) or tethered (brought-in) internet connectivity, or a mixture of both. Vehicles with embedded connectivity are equipped with a built-in modem to directly receive cellular data, while those with tethered connectivity borrow the driver’s smartphone data to access the Internet (similar to WI-FI hotspots).
AT&T In-car Wi-Fi is an internet data plan that works with your vehicle’s built-in Wi-Fi hotspot. Select a plan to start using your car’s Wi-Fi-enabled features, and let your passengers watch movies, play games, and more—each from their favorite screen.

## Slide 31: Industry analysis
1. Competition in the industry
2. Potential of new entrants into the industry
3. Bargaining power of suppliers
4. Bargaining power of customers
5. Threat of substitute products

## Slide 32: Industry analysis
1. Competition in the industry
Medium, fewer similar products in the early stage.
2. Potential of new entrants into the industry
High, because the will be more manufacturers investing in research and development.

## Slide 33: Industry analysis
3. Bargaining power of suppliers
High, it’s a important safety issue to vehicle.
4. Bargaining power of customers
Low, because of the Novelty of product.

## Slide 34: Industry analysis
5. Threat of substitute products
Medium, Some functions for diagnosing the health of components are now integrated into the car chip.

## Slide 35: Industry analysis
1.The growing market size of electric vehicle
2.Attract investment cooperation from insurance companies
1.It can respond to problems in the car faster than manual inspection
2.A safe driving environment is important
1.Diagnosing the health of components may be integrated into the car chip.
1.Long product life cycle
2.Severe standard of safety issue makes a higher cost

## Slide 36: Conclusion
Planning the SoC that combines with multiple functions for responding to different situations during driving
  Vary types of sensors that can detect vehicles’ health
  WRX design for fast respond and power management
  DVFS and energy harvesting technology focus on further low-power SoC design
  AIoT collects and computes the data generated by the SoC for different kinds of applications

## Slide 37: References
Sensors
https://www.allaboutcircuits.com/technical-articles/mems-ic-capacitive-humidity-sensor-basics/
https://www.siliconsensing.com/technology/mems-accelerometers/
https://www.youtube.com/watch?v=wpAA3qeOYiI
https://www.analog.com/en/design-notes/a-simple-thermistor-interface-to-an-adc.html
Tx & Rx
“IEEE 802.11-Enabled Wake-Up Radio: Use Cases and Applications”
https://wics.engin.umich.edu/wp-content/uploads/sites/35/2020/05/Brown_ISSCC2020.pdf
https://innovationatwork.ieee.org/wake-up-radio-infographic/
https://www.ericsson.com/en/blog/2017/12/wake-up-radio--a-key-component-of-iot
“Low-Power RFED Wake-Up Receiver Design for Low-Cost Wireless Sensor Network Applications”
"Communication Integrated Circuits."

## Slide 38: References
AIoT System
https://www.hindawi.com/journals/wcmc/2022/2287776/
https://www.cadence.com/zh_TW/home/solutions/automotive-solution.html
https://community.cadence.com/cadence_blogs_8/b/breakfast-bytes/posts/tensilica-security
https://www.cadence.com/content/dam/cadence-www/global/en_US/documents/tools/ip/design-ip/multi-speed-ethernet-automotive-application-ip-br.pdf
https://prodigytechno.com/difference-between-lin-can-and-flexray-protocols/
https://www.2cm.com.tw/2cm/zh-tw/archives/4E0D19A85F744843ADB63C5D2C65F080
https://www.allaboutcircuits.com/technical-articles/mems-ic-capacitive-humidity-sensor-basics/
https://link.springer.com/chapter/10.1007/978-981-16-2354-7_34
Power Management
  The definitive guide to ARM Cortex-M0/M0+: Low-power states - Embedded.com
  Arm Cortex-M0+ Sleep Modes - Developer Help (microchipdeveloper.com)
  Dynamic Voltage and Frequency Scaling (DVFS) - Semiconductor Engineering (semiengineering.com)
  https://zh.wikipedia.org/zh-tw/%E5%8A%A8%E6%80%81%E6%97%B6%E9%92%9F%E9%A2%91%E7%8E%87%E8%B0%83%E6%95%B4

## Slide 39: Team Member task partition
Introduction -all
System Architecture -all
Technology
  Sensors -徐詠祺
  Tx & Rx -張睿紘
  DVFS -張文彥
  AIoT System -楊文彣
Industry Analysis -王瑞賢
Conclusion -all