## Slide 1
Group 6
107003815 鄭良加 107062803 江崑祺 107062808 陳勇志 107062811 陳奕華 108062601 郭偉祥 108064551 簡瑜成
In-depth Scene Exploration and Reconstruction System
”
SoC Presentation, 2020/01/08

## Slide 2: Outline
Application Scenario
System Architecture
Specification
Edge Server & Display
Porter’s 5 Force Analysis
Team Member Task Partition

## Slide 3: Application Scenario

## Slide 4: Target Market
急難救助（公益） 、地形探勘、巡訪
  難以抵達（上山、下海、半封閉環境與倒塌建築）
  情境險惡、地形複雜
避免將人員置於險境
新科技導入
  運用最少人力
  完善環境探測
Notes: 希望利用無人機的方式，進入人類無法輕易抵達的區域，進行整體環境的探勘、巡訪，並回傳收集到的相關環境數據進行環境的建模，利用這樣的方式讓相關人員能在不深入險境的情況下，進行任務的規畫以及推演，盡可能地避免將人員置於險境，以最少的人力，做到最完善環境的探測。

## Slide 5: Cave
Disaster Area
Quarry
Application Scenario

## Slide 6: Application Scenario
無人載具 （ 空中或水下）
  物資投遞
定位技術
多 sensor 感應融合
3D 建模（地形探勘）
通訊技術
邊緣即時運算
實境呈現
泰國少年足球隊員和教練受困圖
未知的作者 的 此相片 已透過 CC BY-NC-ND 授權
Notes: 泰國 睡美人洞

## Slide 7: System Architecture

## Slide 8: System Architecture
未知的作者 的 此相片 已透過 CC BY-SA 授權
Edge Server
GPU
CPU
Drone
Explorer
Mapping/
Reconstruction
Lidar
Communication
SLAM
5G system
Life sensor
Information collector
Camera
Camera
5G
Drone
Transporter
Drone
Transporter
Drone
Transporters
Mapping/
Reconstruction
Lidar
Communication
SLAM
5G system
Life sensor
Information collector
Camera
Display (VR)
User
Headset
Gesture
Response
System
Camera
Head Motion
Audio
Audio sensor
WiGig (VIVE)
AI Chip

## Slide 9: Drone Specification

## Slide 10: Drone Specification
FOV 78.8° 28 mm (35 mm format equivalent) f/2.2
Lens
1/2.3” CMOS 12.35 MP
Sensor
C4K: 4096×2160 24p
4K: 3840×2160 24/25/30p
2.7K: 2720x1530 24/25/30p
FHD: 1920×1080 24/25/30/48/50/60/96p
HD: 1280×720 24/25/30/48/50/60/120p
Video Resolution
280 Mbps
Max Video Bitrate
3830 mAh
Battery
65 KM/H
Max Speed
30 minutes
Flight Time
11.4 V
Voltage
https://www.dji.com/tw/mavic/info#specs
Notes: https://www.dji.com/tw/mavic/info#specs

## Slide 11: Chiplet Architecture (Lego-like Hardened IP)
Notes: https://www.mccoycomponents.com/blog/view/understanding-chiplet-in-one-article
https://www.eetimes.com/chiplet-effort-plays-first-proposals/#
https://www.slideshare.net/Netronome/odsa-subproject-launch-136606539
https://www.anandtech.com/show/14211/intels-interconnected-future-chipslets-emib-foveros
https://www.mooreelite.com/?p=6793

## Slide 12: Our SoC Chip (Chiplet)
5G
LiDAR
SLAM
CPU
&
GPU
HBM2
HBM2
Item | Spec.
CPU | 8-core NVIDIA Carmel Arm®v8.2 64-bit CPU 8MB L2 + 4MB L3
GPU | 512-core NVIDIA Volta™ GPU with 64 Tensor Cores
LIDAR | Vertical angle of view: 15° Horizontal angle of view: 120° Sampling rate: 10Hz
SLAM | 30 cm resolution for 3D modeling
HBM2 | Density: 2 GB Bandwidth: 128 GB/s
5G | Sub-6 GHz Transfer BW: 280MB/s Video: 220MB/s for 480p Lidar + SLAM: 20MB/s
Notes: https://www.microway.com/hpc-tech-tips/amd-epyc-rome-cpu-review/microway-2ndgen-epyc-rome-chipletdie/
https://custompc.raspberrypi.org/articles/preview-amd-zen-2-ryzen-9-3900x
https://www.novuslight.com/silc-technologies-demonstrates-silicon-photonics-lidar-chip_N9055.html
https://www.ansforce.com/post/S1-p1462

## Slide 13: Jetson AGX Xavier
 | Jetson AGX Xavier Series
 | AGX Xavier
AI 效能 | 32 TOPS
GPU | 512-core NVIDIA Volta™ GPU with 64 Tensor Cores
CPU | 8-core NVIDIA Carmel Arm®v8.2 64-bit CPU 8MB L2 + 4MB L3
記憶體 | 16 GB 256-bit LPDDR4x 136.5GB/s
儲存空間 | 32GB eMMC 5.1
電源 | 10W ¦ 15W ¦ 30W
CSI 相機 | 至多 6 cameras (藉由虛擬通道可拓展至 36 個) 16 lanes MIPI CSI-2 ¦ 8 lanes SLVS-EC D-PHY 1.2 (up to 40 Gbps) C-PHY 1.1 (up to 59 Gbps)
影片編碼 | 2x1000MP/sec 4x 4K @ 60 (HEVC) 16x 1080p @ 60 (HEVC) 32x 1080p @ 30 (HEVC)
影片解碼 | 2x1500MP/sec 2x 8K @ 30 (HEVC) 6x 4K @ 60 (HEVC) 26x 1080p @ 60 (HEVC) 72x 1080p @ 30 (HEVC)
DL 加速器 | 2x NVDLA Engines
視覺加速器 | 7-Way VLIW Vision Processor
https://devblogs.nvidia.com/nvidia-jetson-agx-xavier-32-teraops-ai-robotics/

## Slide 14: HBM2 (High Bandwidth Memory)
High Bandwidth/Channels/Bits
Small form factor、Power efficiency
Base Die : Memory controller
DRAM Die(2~8) : TSV(矽通孔) 互連上下裸晶
Vendor
  Samsung
  SK Hynix
Notes: https://blocksandfiles.com/2019/08/12/sk-hynix-high-bandwidth-memory/
https://benchlife.info/sk-hynix-hbm2-will-mass-production-q3-and-for-amd-polaris-03092016/
https://tcuvelier.wordpress.com/2019/03/25/samsung-annonce-ses-puces-de-memoire-hbm2e-nom-de-code-flashbolt/

## Slide 15: Dimensity 1000
https://www.anandtech.com/show/15155/mediatek-announces-dimensity-1000-soc-back-to-the-highend-with-5g
https://dacota.tw/blog/post/100672
2.3Gbps
Peak Upload Speed
未知的作者 的 此相片 已透過 CC BY-SA 授權
Beamforming technical can reduce unnecessary power consumption for signal transmission.
It will be helpful for extending time of exploration.

## Slide 16: LiDAR
位置 | 感測技術 | 規格 | 說明
前方 | Lidar | 反射率 10% 下, 測距 25m 水平 Fov: 120 度 垂宜 Fov: 15 度 更新頻率: 10Hz 功率: 13W | 同時做 Point Cloud 採集 13W
上方 | 紅外 | 測距: 10cm-80cm 功率: Typ. 30mA@5V | 150mW
下方 | 紅外 | 測距: 10cm-80cm 功率: Typ. 30mA@5V | 150mW
後方 | 紅外 | 測距: 10cm-80cm 功率: Typ. 30mA@5V | 150mW
左側 | 超音波 | 測距: 10cm-100cm 功率: Typ. 2mA@5V 感測角度: < 15 度 | 10mW
右側 | 超音波 | 測距: 10cm-100cm 功率: Typ. 2mA@5V 感測角度: < 15 度 | 10mW
前視光達系統
後視紅外測距
下視紅外測距
右視超音波
左視超音波
Notes: 參數及應用需求評估
掃描頻率 f 及感測距離 D:
  需求必要條件: 物體秒速度 v / f < D, 每次掃描間格的前進距離需小於 D
水平和垂真角解析度 Ha, Va
  決定被掃描面可被感知的表面高低落差
  dv=2*pi*D/360*Va
  dh=2*pi*D/360*Ha
  規格對無人機SLAM 重要性： 低
建議規格:掃描頻率 10Hz, 無人機飛行速度 5m/s, Lidar 感測距離 25m

## Slide 17: Energy Efficient SLAM Accelerator
Tracking: Camera and Lidar motion estimation
  Real-time restrictions, high FPS, mostly fixed-point
Mapping: Estimates 3D positions of feature points
  Semi-real-time, mostly floating-point
Loop Closure: Global trajectory optimization
  Extremely high computing load, mostly floating-point
技術 | 優勢 | 劣勢 | 開發難度 | 成本 | 
Lidar SLAM | 定位構圖精度高 路線規劃簡單 無累計誤差 | 壽命問題(1000h每天使用約兩年更換)、成本高、受Lidar探測範圍限制 | 較低 | 高 | 地圖缺乏語意
Visual SLAM | 體積小、功耗低、使用壽命長、安裝方式多元 | 數據量大、對處理器有更高性能需求、受光照影響大、高動態環境精度下降、對場景複雜度要求高 | 高 | 低 | 具語意訊息

## Slide 18: AI Algorithm
A Trail DNN node applies HarDNet (清大林永隆教授實驗室) .
An object DNN node applies SSD-HarDNet68 (清大林永隆教授實驗室)
A node runs the DSO visual odometry algorithm, whose output is converted to a camera-centric depth map for obstacle detection and avoidance.
Mark the objects
Make our drone fly along traces we desired.
Pick up the object which will affect flight
參考此篇論文的結構 https://arxiv.org/pdf/1705.02550.pdf
Toward Low-Flying Autonomous MAV Trail Navigation using Deep Neural Networks for Environmental Awareness

## Slide 19: Edge Server & Display

## Slide 20: Edge Server
Making the module
Recognition environment
Project to VR
LiDAR and SLAM information
Notes: Nvidia Jetson Xavier
本身具有CPU GPU與AI加速器 且其低功耗的表現使我們選擇了這塊開發版

## Slide 21: VR Headset
• Prototype – HTC VIVE Pro
• Interact with the virtual reconstructed world
• Head motion – Gyroscope
• Gesture – Camera
• Voice – Microphone
• WiGig – Wireless Projection
• IEEE 802.11ad
• 2.4GHz, 5GHz, 60GHz
• Up to 8 Gbps
https://www.vive.com/tw/wireless-adapter/
Notes: 60GHz=>波長短(mmWave)、傳輸距離短(無法穿牆、約10M)
handoff 技術能使網絡產品在離開最佳工作距離後，自動切換至連接距離更長的 2.4GHz 或 5GHz Wi-Fi

## Slide 22: Porter’s 5 Force Analysis

## Slide 23: Porter’s 5 Force Analysis
買方的議價能力
  低，市場上暫無類似產品
供應商的議價能力
  高，部分元件或技術只有單一廠商提供
潛在進入者的威脅
  中，工研院目前研發「無人機隧道飛行解決方案」
替代品的威脅
  中，履帶機器人也可達到類似效果
現有競爭者的威脅
  低，市場上暫無類似產品

## Slide 24: Team Member Task Partition

## Slide 25: Team Member Task Partition
市場評估-產品定位 – all
五力分析 – 簡瑜成
技術分析
Drone:
Communication: 5G - 江崑祺
Localization: SLAM - 鄭良加
Mapping/Reconstruction : LiDAR, structure from motion, sensor fusion - 陳勇志
AI: obstacle detection and avoidance, path planning strategy - 郭偉祥
Edge Server - 陳奕華
3D Display, VR - 簡瑜成
規格訂定 – 江崑祺
系統架構相關流程圖 – 陳奕華
Report 彙整 – 陳勇志、江崑祺、陳奕華、郭偉祥、鄭良加、簡瑜成
Chiplet package technical - 鄭良加
HBM2 - 鄭良加

## Slide 26: Reference

## Slide 27: Reference
5G
  https://kknews.cc/zh-tw/tech/kxngorr.html
  https://kknews.cc/zh-tw/tech/n4kb83.html
  https://meethub.bnext.com.tw/%E3%80%905g%E7%A7%91%E6%99%AE%E3%80%91%E5%8F%AA%E8%A6%819%E5%BC%B5%E5%9C%96%EF%BC%8C%E7%9C%8B%E6%87%82%E4%BB%80%E9%BA%BC%E6%98%AF5g%EF%BD%9C%E5%A4%A7%E5%92%8C%E6%9C%89%E8%A9%B1%E8%AA%AA/
  https://www.bnext.com.tw/article/54075/5g-4g-difference
SLAM
  https://deepai.org/publication/eslam-an-energy-efficient-accelerator-for-real-time-orb-slam-on-fpga-platform
  https://kknews.cc/zh-tw/tech/grqxjv9.html
  https://www.leiphone.com/news/201607/GLQj0wrjKD4eHvq5.html
Edge server
  https://twitter.com/geoslamltd/status/576340766605361152
  https://en.wikipedia.org/wiki/WiGig
  https://shilfa.com/argentina/map-on-mars-with-lidar-equipped-space-drones/
  https://www.coolaler.com/threads/intel-xe-gpu.357788/

## Slide 28: Reference (Cont’d)
LiDAR
  IR sensor: https://global.sharp/products/device/lineup/data/pdf/datasheet/gp2y0a21yk_e.pdf
  超音波: https://shop.cpu.com.tw/product/45466/info/
  3D lidar: https://www.sick.com/tw/zf/detection-and-ranging-solutions/3d-lidar/mrs1000/mrs1104c-011010/p/p495197?ff_data=JmZmX2lkPXA0OTUxOTcmZmZfbWFzdGVySWQ9cDQ5NTE5NyZmZl90aXRsZT1NUlMxMTA0Qy0wMTEwMTAmZmZfcXVlcnk9JmZmX3Bvcz0yJmZmX29yaWdQb3M9MiZmZl9wYWdlPTEmZmZfcGFnZVNpemU9OCZmZl9vcmlnUGFnZVNpemU9OCZmZl9zaW1pPTkyLjA=
VR
  https://en.wikipedia.org/wiki/IEEE_802.11ad
  https://ieeexplore.ieee.org/document/8316630
  https://www.vive.com/tw/wireless-adapter/
HBM2
  https://blocksandfiles.com/2019/08/12/sk-hynix-high-bandwidth-memory/
  https://benchlife.info/sk-hynix-hbm2-will-mass-production-q3-and-for-amd-polaris-03092016/
  https://tcuvelier.wordpress.com/2019/03/25/samsung-annonce-ses-puces-de-memoire-hbm2e-nom-de-code-flashbolt/

## Slide 29: Reference (Cont’d)
Chiplet
  https://www.mccoycomponents.com/blog/view/understanding-chiplet-in-one-article
  https://www.eetimes.com/chiplet-effort-plays-first-proposals/#
  https://www.slideshare.net/Netronome/odsa-subproject-launch-136606539
  https://www.anandtech.com/show/14211/intels-interconnected-future-chipslets-emib-foveros
  https://www.mooreelite.com/?p=6793
Drone
  https://www.dji.com/tw/mavic/info#specs