## Slide 1: 3D Sensing for vehicle technologies
通訊所
110064533
陳劭珩

## Slide 2: Outline
Introduction
Technology
Applications
Conclusion
References

## Slide 3: Introduction
Why radar?
  It’s under-researched
  There is no dominant product or company in the market yet
  It has some irreplaceable advantages
    Long detection range (up to 300 m)
    All-weather operation
    Low power consumption
    Most importantly, low cost
What radar? Specifically?
  FMCW radar means an antenna system that transmits and receives EM waves with certain modulation to achieve certain task
    Frequency-Modulated Continuous-Wave, FMCW

## Slide 4: Technology
FMCW radar fundamentals
  Off-the-shelf automotive radars operate with a sequence of linear FMCW signals to simultaneously measure range, angle, and velocity
  The automotive radar is allowed to use 2 frequency bands in mmwaves
    24 GHz (24~24.25 GHz)
    77 GHz (77~79 GHz)
  There is a trend towards 77 GHz for several reasons:
    Larger bandwidth
      76–77 GHz for long-range
      77–81 GHz for short-range
    Higher Doppler resolution
    Smaller antennas with sub-wavelength sized
  Different radar devices vary in their sensing capabilities
    Different radar device normally means different modulation patterns

## Slide 5: Technology
Fun facts about frequency bands
  Licensed-band in 5G Spec
    FR1 410 MHz – 7.125 GHz
    FR2-1 24.25 GHz – 52.6 GHz
    FR2-2 52.6 GHz – 71 GHz
  Up to 100 GHz belongs to 5G, but above 71 GHz are not licensed
    Up to 6 GHz belongs to 4G
  Aside from licensed-bands, there are also private 5G (Local 5G) bands,
  the specific regulations different from country to country
    e.g. 4.6 GHz – 4.9 GHz is a private 5G band in Japan
  How expensive are the frequency bands in 5G in Taiwan?
    A 15 year authorization cost $150 billion NTD
    1 MHz bandwidth worth $200 ~ 500 million NTD

## Slide 6: Technology
Modulation patterns
  Unmodulated CW
    This modulation pattern is used for some mmwave communication signals
  Fast chirp FMCW (Sawtooth modulation)
    This modulation pattern is used in a relatively large range (maximum distance) combined with a negligible influence of Doppler frequency (for example, a maritime navigation radar).
      Account for 90% of the modulation we probably going to seen in out daily lives

## Slide 7: Technology
Modulation patterns
  Slow chirp FMCW (Triangular modulation)
    This modulation pattern allows easy separation of the difference frequency of the Doppler frequency
  Pulsed CW (Square-wave modulation)
    This modulation is used for a very precise distance measurement at close range by phase comparison of the two echo signal frequencies.
  FSK (Stepped modulation)
    This is used for interferometric measurements and expands the
    unambiguous measuring range.

## Slide 8: Technology
FMCW signal is characterized by the following parameters
  the carrier frequency
  the sweep bandwidth
  the chirp duration
  the slope
FMCW waveform

## Slide 9: Technology
FMCW waveform
  One FMCW waveform is referred to as a chirp
  One radar transmission is a frame of chirps equally spaced by chirp cycle time
    The total time is called frame time (time on target, TOT)
  In order to avoid the need for high-speed sampling, a frequency mixer combines the received signal with the transmitted signal to produce two signals
    sum frequency
    difference frequency

## Slide 10: Technology
FMCW waveform
  Then, a low-pass filter is used to filter out the sum frequency component and obtain the IF signal (Intermediate Frequency, IF)
    In this way, FMCW radar can achieve GHz with only MHz sampling
  Resulting complex exponential IF signal
  Next, the IF signal is sampled N times by an ADC converter, resulting in a discrete-time complex signal

## Slide 11: Technology
FMCW signal processing
  Multiple frames of chirp signals are assembled into a 2D matrix
    The dimension of the sampling points within a chirp is referred to as fast time
    The dimension of the chirp index within one frame is referred to as slow time
  Next, a range FFT is applied in the fast-time dimension to resolve the frequency change, followed by a Doppler FFT in the slow-time dimension to resolve the phase change.
    As a result, we obtain a 2D complex-valued data matrix called the Range–Doppler map, RD map

## Slide 12: Technology
FMCW radar detection pipeline
  First, RD maps are integrated coherently along the virtual receiver dimension to increase the SNR
    e.g. say, we have a simple MIMO radar system with 4 Tx and 4 Rx antenna, which means we can synthesize a virtual array with 4 x 4 = 16 channels
  Then, a CFAR detector is applied to detect peaks or estimate the noise level in the RD map
  Finally, the DOA estimation method is applied for angle estimation
    for conventional radars, only azimuth angle is resolved
    for next-generation radars, both azimuth and elevation angles can be resolved
  The output of the radar is a point cloud with measurements of range, Doppler, and angle

## Slide 13: TI AWR2944EVM
Features
  76 to 81 GHz mmwave radar sensor
  Onboard four-transmit four-receive (4Tx / 4Rx) antenna
  On-chip C66x DSP core and Arm Cortex-R5F controller
  On-chip hardware accelerator for FFT
AWR2944 Evaluation Module (EVM) ($549 USD)
Notes: CAN-FD Protocol, Controller Area Network Flexible Data-Rate
I2C Bus, Inter-Integrated Circuit Bus

## Slide 14: TI AWR2944 Spec
Parameters
Notes: CAN-FD Protocol, Controller Area Network Flexible Data-Rate
I2C Bus, Inter-Integrated Circuit Bus

## Slide 15: TI AWR2944 Spec
Functional Block Diagram
Notes: CAN-FD Protocol, Controller Area Network Flexible Data-Rate
I2C Bus, Inter-Integrated Circuit Bus

## Slide 16: TI AWR 2944 Spec
Functional Block Diagram
Notes: CAN-FD Protocol, Controller Area Network Flexible Data-Rate
I2C Bus, Inter-Integrated Circuit Bus

## Slide 17: Applications
Active safety functions
  Automatic Emergency Braking (AEB)
  Forward Collision Warning (FCW)
Autonomous driving
  Provide range and velocity estimation for the decision fusion algorithm
Non-contact vital sign detection
  Breath rate
  Heart rate
    Use cases
      Burn patients
      Patients that have been isolated due to infectious disease

## Slide 18: Opponents
Vision – Comma ai Driver Assistance System ($2499 USD)
  Camera
    Three 1080p cameras w/ 120 dB of dynamic range: dual-cam 360° vision
    One narrow cam to see far-away objects
  Processor
    Qualcomm Snapdragon 845
  Storage
    32 GB built-in storage
    1TB Samsung 980 NVMe SSD
  Connectivity
    LTE
    Wi-Fi
    High-Precision GPS
  Night-vision
    IR LEDs for interior night-vision monitoring

## Slide 19: Opponents
LiDAR – Velodyne HDL-64E LiDAR Sensor ($80000 USD)
  Sensor
    Time of Flight Distance Measurement with Intensity
    64 channels
    Measurement Range: Up to 120 m
    Single or Dual Returns
    Field of View (Vertical): +2.0° to -24.9° (26.9°)
    Angular Resolution (Vertical): 0.4°
    Field of View (Horizontal): 360°
    Angular Resolution (Horizontal/Azimuth): 0.08° – 0.35°
    Rotation Rate: 5 Hz – 20 Hz
  Laser
    Laser Product Classification: Class 1 Eye-safe
    Wavelength: 903 nm
    Dynamic Laser Power Selection for Larger Dynamic Range

## Slide 20: Conclusion
SWOT
  Strengths
    Long detection range
    All-weather operation
    Low power consumption
    Low cost
  Weaknesses
    Low angular resolution
    Hard to detect stationary object
  Opportunities
    Autonomous driving
    Vital sign detection
  Threats
    Vision
    LiDAR

## Slide 21: References
Zhou, Yi, et al. "Towards Deep Radar Perception for Autonomous Driving: Datasets, Methods, and Challenges." Sensors 22.11 (2022): 4208. (https://www.mdpi.com/1424-8220/22/11/4208)
AWR2944EVM (https://www.ti.com/tool/AWR2944EVM)
AWR2944 Spec (https://www.ti.com/product/AWR2944)
Comma ai (https://comma.ai/shop/comma-three)
Velodyne 64-line LiDAR (https://www.neuvition.com/media/blog/lidar-price.html)